## Slide 1: A 130 nm Sub-VT Power-Gated Processor for Body Sensor Network Applications
Yanqing Zhang
Yousef Shakhsheer

## Slide 2: Motivation
To reduce energy while idling without degrading performance, especially in battery constrained applications
i.e. ECG algorithm – Sampling rate is 1 kHz
Average time to process one sample is 20 µs
980 µs of idle time
Opportunity for savings!

## Slide 3: Methodology
RTL
CPF
Place files in RTL Compiler
Load Encounter
Commit CPF in Encounter

## Slide 4: Methodology
Move power domain macro modules
Encounter leaves a row and column between different domains

## Slide 5: Methodology
Add power switches in respective power domain

## Slide 6: Methodology
Specify switch topology

## Slide 7: Methodology
Specify Global Net Connections
Verilog has no concept of VDD and GNDs, let alone different power domains
Use “Override prior connection” button to your convenience
Important step in flow

## Slide 8: Methodology
A successfully floorplanned design that is power-gate ready
Rest of flow is same as SOC place and route flow
Yay! So CPF retains the convenience synthesis flow brings us, with powerful flexibility for low power design

## Slide 9: Our design

## Slide 10: Header Topologies – Lumped vs Distributed
Metric | Best Choice
IR Drop | Lumped
Delay degradation | Distributed
Power gating savings | Distributed
Recovery time | Lumped
Breakeven cycles | Distributed
Ease of Design | Lumped

## Slide 11: What we learned
Required to break the VDD connection on the standard cell libraries
Inherent VDD makes our life harder

## Slide 12: What we learned
Our set of tools will not automatically characterize headers and decide on sizing
Header sizing is hard
Trade offs in metrics
Chart: 
| 8.4 um | 16.8 um | 33.6 um | 67.2 um | 134.4 um
Switching Time Overhead | 1.2538 | 1.1582 | 1.1103 | 1.087 | 1.0744

## Slide 13: Header Sizing
Chart: 
| 8.4 um | 16.8 um | 33.6 um | 67.2 um | 134.4 um
Vrail Min | 0.94994 | 0.97102 | 0.98369 | 0.99124 | 0.99588
Chart: 
| 8.4 um | 16.8 um | 33.6 um | 67.2 um | 134.4 um
Energy During Power Gating | 0.0038304 | 0.0066116 | 0.012142 | 0.023087 | 0.045671

## Slide 14: Header Sizing
Chart: 
| 8.4 um | 16.8 um | 33.6 um | 67.2 um | 134.4 um
Recovery Time | 0.18969 | 0.089811 | 0.045037 | 0.020609 | 0.0095329
Chart: 
| 8.4 um | 16.8 um | 33.6 um | 67.2 um | 134.4 um
Break Even Cycles | 71.852 | 149.1649 | 286.6511 | 526.5026 | 979.0692

## Slide 15: Class Specific Action & Future Work
Using CPF to do header insertion
Making tutorial
Script based flow
Tool for analyzing header sizing